## Slide 1: Thermo-Hydraulics (THM) MOOSE Module Utah Forge Simulation One Fracture Model
Intern: Benjamin Willis
Mentor: Robert Podgorney

## Slide 2
(0,0,0)
(0,0,-2057)
(1122.6,0,-2632.1)
(1122.4,0,-2531.9)
(1,0,-1957)
(1,0,0)
I.D = 0.076 m for 10 perfs
I.D = 0.076 m for 10 perfs
I.D = 1 m
I.D = 0.18 m
Perf diameter = 3/8 in = 0.009525 m

## Slide 3
injection_pipe
production_pipe
jct1
pipe2
fracture3_perf1
fracture3
fracture3_perf2
jct4
Jct_fracture3_perf1
Jct_fracture3_perf2
jct5
jct8
pipe5
inlet
outlet
jct2
pipe3
jct3
pipe4
jct6
pipe6
jct7
pipe7
fracture3 injection well distance ~= 3317 m ~= 10887 ft

## Slide 4
2057 m
1030 m
134 m
96 m
1957 m
Model Pipe Lengths (all approximated)
1 m
98 m
fracture3 injection well distance ~= 3317 m ~= 10887 ft
1 m

## Slide 5: Parameters
Component Name | Parameters Used
inlet | m_dot = 5 kg/s T_in = 25°C
outlet | p = 2 MPa (~= 145 PSI)
Perforations | Diameter = 0.009525 m, 10 perfs assumed  Diameter = 0.09525 m Length = 1 m
Fractures | Diameter = 2 m Length = 98 m
All pipes | # of elements = 200 custom_closures used (f = 0.0167, Hw = 2000)
Temperature with Elevation | Linear interpolation between 25°C at z = 0 m 196°C at z = -2800 m
Pressure with Elevation | Linear interpolation between 101.325 kPa at z = 0 m 25.1865e3 kPa at z = -2800 m

## Slide 6: Fluid Properties Used
Modules/FluidProperties Name | Parameters Used
water | type = StiffenedGasFluidProperties gamma = 2.35 (heat capacity ratio) cv = 1816 (Constant volume specific heat) q = -1.167e6 (defines zero point of internal energy) p_inf = 1e9 (stiffness parameter) mu = 1e-4 Pa*s (Dynamic viscosity) q_prime = 0 (Default)

## Slide 7: Heat Structure Materials
HeatStructureMaterials Name | Parameters Used
mild_steel (used for pipe wall) | rho = 7850 kg/m3 cp = 510.8 J/(kg*K) k = 60 W/(m*K)
cement | rho = 2400 kg/m3 cp = 920 J/(kg*K) k = 0.29 W/(m*K)
rock | rho = 2750 kg/m3 cp = 830 J/(kg*K) k = 3 W/(m*K)

## Slide 8: Preconditioning Used
Preconditioner Name | Parameters Used
pc | type = SMP full = true

## Slide 9: Executioner Used

## Slide 10: Heat Structures for pipes
R = 50 m
INNER_RADIUS = 0.09 m = pipe radius
Temperature BCs: based on Temperature with Elevation
pipe
pipe wall
cement
rock
Width pipe wall = 0.00635 m
Width cement = 0.0051 m
Width rock = 49.95 m

## Slide 11: Heat Structures for fractures
R = 50 m
INNER_RADIUS = 0.5 m or 1 m = fracture radius
Temperature BCs: based on Temperature with Elevation
fracture (treated as a pipe)
rock
Width rock = 50 m

## Slide 12: Calculating Fracture Permeability Using Darcy’s Law
Equation 1
Equations 1 and 2
Solve for k
Equation 2
Use , and at inlet and outlet of fracture and compare value

## Slide 13: 1 Fracture Study
Done With both Inlet and Exit Perforations
5 kg/s
Fracture diameter = 2 m
10 inlet and exit perforations

## Slide 14: Paraview at ~= 60,000s

## Slide 15
Pressure at Injection and Production Points

## Slide 16
Pressure Drop Across EGS

## Slide 17
Pressure Drop Across EGS

## Slide 18
Pressure Across EGS

## Slide 19
Pressure Across Fracture

## Slide 20
Flow Distribution

## Slide 21
Fracture Inlet vs Outlet Temperature

## Slide 22
Fracture Permeability